## Slide 1: Digitale Integrierte Schaltungen 2018 WS
Prof. Axel Jantsch

## Slide 2: Verwendete Literatur
Lehrbuch Digitaltechnik
Jürgen Reichardt
3. Auflage, Oldenbourg 2013
https://www.degruyter.com/viewbooktoc/product/228761
Kapitel: 2,4, 7, 9, 10, 11, 12, 13, 14, 15, 16, 17
„Logic Synthesis in a Nutshell“,
Jie-Hong Jiang and Srinivas Devadas,
http://www.sciencedirect.com/science/article/pii/B9780123743640500138
Kapitel: 61, 6.2, 6.3, 6.4

## Slide 3: Weiterführende Literatur
Entwurf von digitalen Schaltungen und Systemen mit HDLs und FPGAs : Einführung mit VHDL und SystemC
Frank Kesel, Ruben Bartholomä
München : Oldenbourg 2013
RTL Hardware Design Using VHDL
P. Pong Chu
Wiley, 2006
http://ieeexplore.ieee.org/xpl/bkabstractplus.jsp?bkn=5237648

## Slide 4
Empfohlene Lektüre für den Abend:

## Slide 5: Vorspann
Was sind integrierte Schaltungen?
Was ist VLSI?
Was sind ASICs?
Was sind SoCs?

## Slide 6
Intel Ivy Bridge
1.4 Billion Transistors
160mm2, 22nm
77W, 3.9 GHz
Intel Tukwila
2.046 Billion Transistors
21.5 x 32.5 mm2, 65nm
170W, 2GHz

## Slide 7
Sun Niagara 3
1 Billion Transistors
16 cores, 377mm2, 40nm
1.67 GHz, 60W
Intel Teraflop
100 Million Transistors
80 cores, 275mm2, 65nm
3.67GHz, 62W

## Slide 8
Intel Westmere Xeon E2
4.31 Billion Transistors
15 cores, 541mm2, 22nm
2.8GHz, 155W

## Slide 9: Intel Skylake Server Architecture
Notes: https://en.wikichip.org/wiki/intel/microarchitectures/skylake_(server)
https://en.wikichip.org/wiki/intel/microarchitectures

## Slide 10: Intel Skylake Server Architecture 10-28 cores (12-30 tiles), 14nm, 694 mm2 (30 tiles)
Cache
L0 µOP cache:
  1536 µOPs/core,
  8-way set associative
  32 sets, 6-µOP line size
L1 I Cache:
  32 KiB/core,
  8-way set associative
  64 sets, 64 B line size
L1D Cache:
  32 KiB/core,
  8-way set associative
  64 sets, 64 B line size
  4 - 5 cycles latency
  Write-back policy
L2 Cache:
  1 MiB/core,
  16-way set associative
  64 B line size
  Write-back policy
  14 cycles latency
L3 Cache:
  1.375 MiB/core,
  11-way set associative,
  shared across all cores
  2,048 sets, 64 B line size
  Write-back policy
  50-70 cycles latency
Notes: https://en.wikichip.org/wiki/intel/microarchitectures/skylake_(server)

## Slide 11: Nvidia Turin TU102
 | Full TU201
Process (nm) | 12
Transistors (billion) | 18.6
Sie size (mm2) | 754
Streaming Multiprocessors (SM) | 72
CUDA Cores | 4608 (64/SM)
Tensor Cores | 576 (8/SM)
RT Cores | 72
Clock (MHz) | ≤ 1500
CUDA TFlops (FP32) | 13.8
L1 Cache (MB) | 6.912
L2 Cache (MB) | 6
Bus width | 384
Power (W) | 200-250
Bandwidth (GB/s) | 672
Notes: Very good description of the Nvidia Turing architecture: https://www.pcgamer.com/nvidia-turing-architecture-deep-dive/
Performance table for Nvidia processors: https://cdn.mos.cms.futurecdn.net/mTXY8cGt2ooCjqMFb7ssKQ.png

## Slide 12: Nvidia Turin TU102
Notes: Very good description of the Nvidia Turing architecture: https://www.pcgamer.com/nvidia-turing-architecture-deep-dive/
Performance table for Nvidia processors: https://cdn.mos.cms.futurecdn.net/mTXY8cGt2ooCjqMFb7ssKQ.png

## Slide 13: Nvidia Turin TU102 Streaming Multiprocessor
Notes: Very good description of the Nvidia Turing architecture: https://www.pcgamer.com/nvidia-turing-architecture-deep-dive/
Performance table for Nvidia processors: https://cdn.mos.cms.futurecdn.net/mTXY8cGt2ooCjqMFb7ssKQ.png

## Slide 14
IBM TrueNorth
5.4 Billion Transistors
4096 cores, 350mm2, 28nm
70mW

## Slide 15: 1965
Gordon E. Moore, "Cramming More Components onto Integrated Circuits", Electronics, pp. 114-117, April 1965.
born 1929

## Slide 16: Moore‘s Law
Gordon E. Moore, "Cramming More Components onto Integrated Circuits", Electronics, pp. 114-117, April 1965.

## Slide 17: CPUs Transistor Count

## Slide 18: CPUs Transistor Count

## Slide 19: Three Main Deflection Points
Mead-Conway Revolution in 1980
Systems-on-Chip in 2000
Multi-Core Revolution in 2010

## Slide 20: 1980 20 000 Transistoren

## Slide 21: Mead-Conway Revolution
Carver Mead and Lynn Conway, Introduction to VLSI Systems, Addison-Wesley, 1980.
1980 – 20 000 Transistors
born 1934
born 1938

## Slide 22: Standard Cells

## Slide 23: Standard Cells

## Slide 24: Standard Cells

## Slide 25: Logic Synthesis
Logic Minimization Algorithms for VLSI Synthesis, Kluver Academic Publisher, Robert K. Brayton, Gary D. Hachtel, Curtis T. McMullen, and Alberto L. Sangiovanni-Vincentelli, 1984.

## Slide 26: 1990 1 000 000 Transistoren

## Slide 27: High Level Synthesis
1990 – 1 000 000 Transistors

## Slide 28: Emergence of Systems on Chip

## Slide 29: Emergence of Systems on Chip

## Slide 30: 2000 20 000 000 Transistoren

## Slide 31: The SoC Revolution
Surviving the SOC Revolution - A Guide to Platform-Based Design, Kluwer Academic Publishers, Henry Chang, Larry Cooke, Merrill Hunt, Grant Martin, Andrew McNelly, and Lee Todd, 1999.
2000 – 20 000 000 Transistors

## Slide 32: Wires Don‘t Scale
Ron Ho, On-chip wires: Scaling and efficiency, PhD thesis, Stanford University, 2003.
Chip size
Reachable
area per
Clock cycle
------------
0.035 µm
------------
0.025 µm
Notes: This assumes that clock frequency scales with transistor delay, which in fact did not happen.

## Slide 33: Capacity Trend
From ISSCC 2018 Technology Trends
Notes: The red dot is a Multi-Chip-Module

## Slide 34: End of Frequency Scaling
From ISSCC 2018 Technology Trends

## Slide 35: Emergence of Networks-on-Chip
Intel Teraflop
Tilera TilePro 64

## Slide 36: The Multicore Revolution - Core Count
From ISSCC 2018 Technology Trends
Notes: The red dot is a Multi-Chip-Module

## Slide 37: Graphics Processors

## Slide 38: The Multicore Revolution
Notes: Nvidia GP104 GPU with 2560 cores

## Slide 39: Performance Growth
Performance as measured by the SPEC INT Benchmark
Computer Architecture, J. Hennessy and D. Patterson, 6th edition, 2018; Figure 1.1 page 3.
Notes: As measured by the SPEC INT Benchmark

## Slide 40: Clock Frequency Growth
Computer Architecture, J. Hennessy and D. Patterson, 6th edition, 2018; Figure 1.11 page 26.

## Slide 41
Notes: https://www.karlrupp.net/2015/06/40-years-of-microprocessor-trend-data/

## Slide 42: Technology Roadmap
Technology node (2-3 Years) scaling -2030:
Performance: >30% more maximum operating frequency at constant energy
Power: >50% less energy per switching at a given performance
Area: >50% area reduction
Cost: <30% wafer cost – 30-35% less die cost for scaled die.
International Roadmap for Devices and Systems
2016 Edition
More Moore White Paper
https://irds.ieee.org

## Slide 43: Technology Roadmap
International Roadmap for Devices and Systems, 2016 Edition
More Moore White Paper, https://irds.ieee.org
PxxMxx notation refers to Pxx: contacted poly pitch and Mxx: metalx pitch in nm.
Acronyms used:
FDSOI: Fully-Depleted Silicon-On-Insulator (FDSOI),
LGAA: Lateral Gate-All-Around-Device (GAA),
VGAA: Vertical GAA,
M3D: Monolithic-3D.
Notes: PxxMxx notation refers to Pxx: contacted poly pitch and Mxx: metalx pitch in nm.
Acronyms used in the table (in order of appearance): FDSOI: Fully-Depleted Silicon-On-Insulator (FDSOI),
LGAA: Lateral Gate-All-Around-Device (GAA), VGAA: Vertical GAA, M3D: Monolithic-3D.
LGAA means that source and drain are beside each other and the channels go horizontally between them;
VGAA means that source and drain are stacked on top of each other and the channels go vertically between them.

## Slide 44: FinFET und Gate All Around
By Navid.paydavosi - CC BY-SA 3.0, https://commons.wikimedia.org/w/index.php?curid=18843888

## Slide 45: Technology Roadmap
 | 2015 | 2017 | 2019 | 2021 | 2024 | 2027 | 2030
Industry labeling | „16/14“ | „11/10“ | „8/7“ | „6/5“ | „4/3“ | „3/2.5“ | „2/1.5“
Metal pitch (nm) | 56 | 36 | 24 | 20 | 12 | 12 | 12
Contacted Poly pitch (nm) | 70 | 48 | 42 | 32 | 24 | 24 | 24
Lg: HP Logic (nm) | 24 | 18 | 14 | 10 | 10 | 10 | 10
Lg: LP Logc (nm) | 26 | 20 | 16 | 12 | 12 | 12 | 12
Vdd (V) | 0.8 | 0.75 | 0.7 | 0.65 | 0.55 | 0.45 | 0.4
Vt : HP (V) | 0.129 | 0.129 | 0.133 | 0.136 | 0.084 | 0.052 | 0.052
Vt : LP (V) | 0.351 | 0.336 | 0.333 | 0.326 | 0.201 | 0.125 | 0.125
Inversion layer thickness (nm) | 1.1 | 1.0 | 0.9 | 0.85 | 0.8 | 0.8 | 0.8
Energy/switching (fJ) | 3.47 | 2.52 | 1.89 | 1.24 | 0.94 | 0.63 | 0.50
International Roadmap for Devices and Systems, 2016 Edition
More Moore White Paper, https://irds.ieee.org
Notes: For comparison, size of silicon atom:
The bond length in SiSi is: 235.2pm = 0.2352nm
Atomic radius ~ 0.11 nm
van der Waals radius ~ 0.219 nm (Radius of atoms in non-bonding atoms)
From: https://www.webelements.com/silicon/atom_sizes.html

## Slide 46: Technology Roadmap
 | 2015 | 2017 | 2019 | 2021 | 2024 | 2027 | 2030
Industry labeling | „16/14“ | „11/10“ | „8/7“ | „6/5“ | „4/3“ | „3/2.5“ | „2/1.5“
SRAM density (Mbit/mm2) | 17 | 29 | 50 | 78 | 217 | 217 | 217
NAND2 density (Mgates/mm2) | 9 | 19 | 33 | 78 | 87 | 87 | 87
FO3 delay(ps) | 14.80 | 11.28 | 11.03 | 8.69 | 9.43 | 8.67 | 8.33
FO3 dynamic power @1GHz (μW) | 3.49 | 1.93 | 1.07 | 0.56 | 0.3 | 0.2 | 0.16
FO3 leakage power (μW) | 0.118 | 0.081 | 0.048 | 0.029 | 0.017 | 0.014 | 0.012
No of wiring layers | 13 | 14 | 15 | 16 | 18 | 22 | 30
International Roadmap for Devices and Systems, 2016 Edition
More Moore White Paper, https://irds.ieee.org

## Slide 47
Moore‘s Law worked from 1962-2018.
When will it end ?

## Slide 48: In 2604